# SWV Working Principle
- SWO (Serial Wire Output)
  - works over SWD (Serial Wire Debugger) interface
  - connected to ITM and SWD, and goes to ST link ckt (usb debugger)
- Cortex M4 and up MPUs have ITM unit
  - Instrumentation Trace Macrocell Unit
  - supports printf style debugging
  - has hardware fifo where printf data is written, and is connected to SWO pin
- MPU has SWD connector (Serial Wire Debugger)
  - 2 pins for debug, 1 for trace
    - Debug: SWDIO: bidirectional data line
    - Debug: SWCLK: clock driven by host
    - Trace: SWO (Serial Wire Output) used for printf functionality
  - alternative to JTAG debugging
- The TRCENA register has to be enabled in order for the fifo to be read/written.
- The ITM_TRACE_EN has to be enabled to utilize port 0 of the ITM trace.
- Wait for the status to be true.
- Write character to port
# Understanding Memory Map of MCU
- System Bus: 32 bits
- Processor can produce 2^32 of different addresses. 4Gb
  - 0x0000_0000 to 0xffff_ffff
- When the processor produces address 0x4002 0000 - 0x4002 03FF on the system bus, it is referring to GPIOA registers. This was given from section 2.3 Memory Map in the reference manual. Pg 65